## Slide 1: Technical User Guide Summary
SSB Retuning Automations (v0.7.3)

## Slide 2: Tool overview
SSB Retuning Automations is an automation platform for SSB retuning projects that can run in GUI or CLI mode or through a Web Interface (using a server/client infrastructure) and orchestrates five functional modules:
  Module 0: Update Network Frequencies.
  Module 1: Configuration Audit & Logs Parser.
  Module 2: Consistency Check (manual Pre/Post).
  Module 3: Consistency Check Bulk (automatic Pre/Post detection by market).
  Module 4: Final Clean-Up.
The main execution lives in "src/SSB_RetuningAutomations.py", where CLI arguments, GUI, configuration persistence, input resolution (folders/ZIP), per-module execution, and artifact versioning are managed.

## Slide 3: Repository technical architecture Main files
Orchestration core
  "src/SSB_RetuningAutomations.py": entry point, CLI/GUI parsing, module routing, batch/bulk execution, and versioning.
Main modules files
  "src/modules/ConfigurationAudit/ConfigurationAudit.py": log parsing and audit workbook construction (Excel + PPT).
  "src/modules/ConfigurationAudit/ca_summary_excel.py": assembly of "SummaryAudit" and discrepancy dataframes.
  "src/modules/ConsistencyChecks/ConsistencyChecks.py": PRE/POST loading, relation comparison, discrepancies, and output export.
  "src/modules/ProfilesAudit/ProfilesAudit.py": profiles audit (integrated into module 1).
  "src/modules/CleanUp/FinalCleanUp.py": final clean-up (base implementation for extension).
Common layer and utilities

## Slide 4: Repository technical architecture Main files (cont.)
  "src/modules/Common/*.py": correction command logic and shared functions.
  "src/utils/*.py": IO, parsing, frequency handling, Excel, pivots, sorting, infrastructure, and timing.

## Slide 5: Inputs, outputs, and content per module Module 0 — Update Network Frequencies
Input
  Input folder (may contain subfolders/ZIPs already supported by the IO layer).
  Logs with an "NRFrequency" table and the "arfcnValueNRDl" column.
Process
  1. Scan logs and detects "NRFrequency" blocks.
  2. Extracts numeric values from "arfcnValueNRDl".
  3. Removes duplicates and sorts frequencies.
  4. Updates the persisted “Network frequencies” configuration for GUI/CLI.
Output
  Does not generate Excel/PPT.
  Updates the persisted network frequency value used for filtering and selection in later runs.

## Slide 6: Inputs, outputs, and content per module Module 1 — Configuration Audit & Logs Parser
Inputs
  Input folder with logs (".log", ".logs", ".txt") or ZIPs resolvable by utilities.
  Frequency parameters:
    "n77_ssb_pre"
    "n77_ssb_post"
    "n77b_ssb"
    allowed SSB/ARFCN lists pre/post.
  Flags:
    "profiles_audit"
    "frequency_audit"
    "export_correction_cmd"
    "fast_excel_export".
Process

## Slide 7: Inputs, outputs, and content per module Module 1 — Configuration Audit & Logs Parser (cont.)
  1. Parses files and extracts MO tables by "SubNetwork" blocks.
  2. Generates one sheet per detected table.
  3. Builds "SummaryAudit" + pivots/auxiliary summaries.
  4. Runs profiles audit if enabled.
  5. Exports CA correction commands if requested.
  6. Generates the summary PPT.
Outputs
  Folder "ConfigurationAudit_<timestamp>_v<version>/".
  Excel file "ConfigurationAudit_<timestamp>_v<version>.xlsx":
    Sheets for each parsed MO table.
    "SummaryAudit".
    NR/LTE parameter discrepancy sheets.
    Summary/pivot sheets by frequencies and relations.
  PPT file "ConfigurationAudit_<timestamp>_v<version>.pptx".
  Optional folder "Correction_Cmd_CA/" with AMOS commands.
Main semantic content

## Slide 8: Inputs, outputs, and content per module Module 1 — Configuration Audit & Logs Parser (cont.)
  SummaryAudit contains rows with:
    "Category", "SubCategory", "Metric", "Value", "ExtraInfo",
    and execution context fields (stage, module, etc. depending on the flow).
  "Value" usually represents a count of impacted nodes/cells/relations.
  "ExtraInfo" contains the NodeId list or a compact discrepancy detail.

## Slide 9: Inputs, outputs, and content per module Module 2 — Consistency Check (Pre/Post)
Inputs
  "input_pre" and "input_post" (or equivalent resolved structure).
  Frequencies "n77_ssb_pre" and "n77_ssb_post".
  Optional reference to PRE and POST "ConfigurationAudit" to enrich target classification.
  Optional list of frequency filters ("cc_freq_filters").
Process
  1. Loads relation tables ("GUtranCellRelation", "NRCellRelation").
  2. Normalizes columns/keys and selects the most recent snapshots by date.
  3. Detect:
    new relations,
    missing relations,
    parameter discrepancies,
    frequency discrepancies,
    summary by PRE/POST frequency pair.

## Slide 10: Inputs, outputs, and content per module Module 2 — Consistency Check (Pre/Post) (cont.)
  4. Classify destination targets as "SSB-Pre", "SSB-Post" or "Unknown".
  5. Exports detailed Excel outputs and correction commands.
Outputs
  "CellRelation_<timestamp>_v<version>.xlsx" (end-to-end relations view).
  "ConsistencyChecks_CellRelation_<timestamp>_v<version>.xlsx" with:
    "Summary"
    "SummaryAuditComparisson" (if there is PRE/POST SummaryAudit)
    "Summary_CellRelation"
    GU blocks: "GU_relations", "GU_param_disc", "GU_freq_disc", "GU_freq_disc_unknown", "GU_missing", "GU_new"
    NR blocks: "NR_relations", "NR_param_disc", "NR_freq_disc", "NR_freq_disc_unknown", "NR_missing", "NR_new"
    optional "GU_all", "NR_all".
  "Correction_Cmd_CC/" with commands per type (new/missing/discrepancies).

## Slide 11: Inputs, outputs, and content per module Module 3 — Consistency Check Bulk
Inputs
  Root folder with subfolders like "yyyymmdd_hhmm_step0" (optionally nested by market).
Process
  1. Detects PRE/POST candidates by the most appropriate date/time.
  2. Excludes folders using a blacklist ("ignore", "old", "bad", "partial", "incomplete", "discard", etc.).
  3. Runs Module 2 for each detected market.
Outputs
  Same output structure as module 2, per market.
  Traceability file "FoldersCompared.txt".

## Slide 12: Inputs, outputs, and content per module Module 4 — Final Clean-Up
Inputs
  Final retune working folder.
Process
  Executes final cleanup policies (structure prepared to expand rules).
Outputs
  Versioned cleanup directory according to the active implementation.

## Slide 13: Configuration Audit module in detail SummaryAudit checks philosophy
SummaryAudit sheet contains a high-level checks table by categories. The flow:
  1. Excludes "UNSYNCHRONIZED" nodes based on "MeContext".
  2. Evaluates NR, LTE, ENDC, Externals, TermPoints, cardinalities, and profiles.
  3. Records each check as a row ("Category/SubCategory/Metric/Value/ExtraInfo").

## Slide 14: Configuration Audit module in detail Operational meaning of SummaryAudit rows
  Category: audited technical domain (NR/LTE/ENDC/MeContext/etc.).
  SubCategory: type of analysis (Audit/Inconsistencies/Profiles).
  Metric: specific rule evaluated.
  Value:
    Integer: number of affected nodes/relations/cells.
    "N/A": not evaluable due to missing columns.
    Text: captured status or error.
  ExtraInfo: list of nodes or bounded detail for troubleshooting.

## Slide 15: Configuration Audit module in detail SummaryAudit checks catalog
MeContext Audit
  total unique nodes and unsynchronized node exclusion.
  "UNSYNCHRONIZED" nodes (excluded from the rest of the audits).
NR Frequency Audit / NR Frequency Inconsistencies
Source tables: "NRCellDU", "NRFrequency", "NRFreqRelation", "NRSectorCarrier", "NRCellRelation", "ExternalNRCellCU", "TermPointToGNodeB", "TermPointToGNB".
Main checks:
  Detection of NR nodes with N77 SSB (band 646600–660000).
  Classification of NR nodes as LowMidBand / mmWave / mixed.
  Nodes whose N77 SSBs are fully within allowed PRE or POST lists.
  Nodes with N77 SSB outside allowed lists.
  Old/new SSB presence per node (only old, only new, both).
  Nodes with NRFreqRelationId in an unexpected format (auto-created outside convention).
  NR relations to old/new SSB.
  NR externals and termpoints pointing to old/new/unknown.
Typical triggering:

## Slide 16: Configuration Audit module in detail SummaryAudit checks catalog (cont.)
  Each check is enabled if the table and minimum required columns exist.
  If columns are missing, a "N/A" status row is added.
  If the table is empty or not found, an informative row "Table not found or empty" is added.
Interpretation:
  "Value > 0" in inconsistencies indicates a real deviation that requires investigation.
  "ExtraInfo" typically lists affected nodes for operational targeting.
LTE Frequency Audit / LTE Frequency Inconsistencies
Source tables: "GUtranSyncSignalFrequency", "GUtranFreqRelation", "GUtranCellRelation", "ExternalGUtranCell", "TermPointToENodeB".
Main checks:
  LTE nodes with old/new SSB.
  Nodes with both old/new or old without new.
  SSB outside the expected pre/post set.
  LTE relations to old/new and parameter discrepancies per cell relation.
  LTE externals OUT_OF_SERVICE for old/new.

## Slide 17: Configuration Audit module in detail SummaryAudit checks catalog (cont.)
ENDC Audit / ENDC Inconsistencies
Source tables: "EndcDistrProfile", "FreqPrioNR".
Main checks:
  "gUtranFreqRef" and "mandatoryGUtranFreqRef" with old/new + N77B combinations.
  Nodes that do not contain the expected frequency combination.
  In "FreqPrioNR": old without new, both present, and parameter mismatch per cell.
Cardinalities Audit / Inconsistencies
Cardinality checks per relation table (per node and/or per cell) to detect overprovisioning or gaps versus expected limits.
Profiles Audit (if enabled)
  Compares PRE/POST profiles by supported profile MO.
  Detects parameter discrepancies between old/new variants.
  Adds results to SummaryAudit and auxiliary detail sheets.

## Slide 18: Consistency Check module in detail Filtering by non-retuned nodes
If a POST SummaryAudit exists, the module obtains PRE/POST node lists and can exclude discrepancies whose target points to nodes that did not complete retune, reducing operational noise.

## Slide 19: Consistency Check module in detail How it detects parameter discrepancies
  1. Selects common PRE and POST relations by composite key:
    GU: typically "NodeId", "EUtranCellFDDId", "GUtranCellRelationId".
    NR: typically "NodeId", "NRCellCUId", "NRCellRelationId".
  2. Excludes control columns (keys, frequency, Pre/Post, Date).
  3. Compares value-by-value across shared columns.
  4. Sets "ParamDiff=True" if at least one column differs.
  5. In GU it ignores "timeOfCreation" and "mobilityStatusNR" to avoid false positives.

## Slide 20: Consistency Check module in detail How it detects frequency discrepancies
  1. Extracts base frequency from relation references ("extract_gu_freq_base" / "extract_nr_freq_base").
  2. Discrepancy rule:
    if PRE had "freq_before" or "freq_after", and POST does not end up in "freq_after", it marks "FreqDiff=True".
  3. Classifies the discrepancy as:
    "FreqDiff_SSBPost" (target identified as SSB-Post),
    "FreqDiff_Unknown" (cannot be associated to a known target).

## Slide 21: Consistency Check module in detail How it detects neighbor discrepancies
They are split into three groups:
  New relations: keys present in POST and absent in PRE.
  Missing relations: keys present in PRE and absent in POST.
  Discrepancies: same key in PRE/POST but with parametric or frequency differences.

## Slide 22: Consistency Check module in detail Content of each ConsistencyChecks output sheet
  Summary: KPIs per table (PRE/POST volume, discrepancies, new/missing, source files).
  SummaryAuditComparisson: diff of SummaryAudit PRE vs POST metrics (without "ExtraInfo" to keep the comparison clean).
  Summary_CellRelation: KPI per "Freq_Pre/Freq_Post" pair and per technology.
  GU_relations / NR_relations: relation universe enriched with target classification and command snippets.
  GU_param_disc / NR_param_disc: common relations with param differences.
  GU_freq_disc / NR_freq_disc: frequency discrepancies to SSB-Post targets.
  GU_freq_disc_unknown / NR_freq_disc_unknown: discrepancies with non-classifiable targets.
  GU_missing / NR_missing: relations removed versus PRE.
  GU_new / NR_new: relations added in POST.
  GU_all / NR_all: optional consolidated dump for extended analysis.

## Slide 23: Input requirements and operational best practices
  Keep market log exports in a consistent structure (especially for bulk).
  Validate that PRE/POST have the same table granularity and consistent naming.
  Validate frequency inputs ("n77_ssb_pre", "n77_ssb_post", "n77b_ssb") before batch execution.
  Correctly configure allowed SSB/ARFCN lists to minimize false positives.
  Run Configuration Audit before Consistency Checks whenever possible.
  Use Bulk mode only with a controlled folder naming convention.
  Review "Summary" and "Summary_CellRelation" first, then then deep-dive into detail sheets (ConfigurationAudit) and discrepancy tabs (ConsistencyCheck).
  Consume "Correction_Cmd_CA" and "Correction_Cmd_CC" as a remediation proposal, not as blind execution.

## Slide 24: Execution Modes and Versioning
  GUI mode: run without CLI arguments.
  CLI mode: run with explicit module and options.
  Web Interfacee: the tool can be run in a server/client infrastructure, accessing the server through a Web Interface where you can unpload your inputs, enqueue different tasks and export the results when finish..
All Generated artifacts include a versioned suffix: "<timestamp>_v<TOOL_VERSION>".
This guarantees traceability and avoids collisions between runs.

## Slide 25: Known limitations and considerations
  The engine depends on log quality and structure: missing columns downgrade checks to "N/A".
  Some rules depend on naming conventions in references (NR/GU relation refs).
  The Final Clean-Up module is prepared to extend operation-specific policies.

## Slide 26: Quick module reference
Module | Main input | Main output | Goal
0 Update Network Frequencies | Logs folder | Persisted config | Update network frequency list
1 Configuration Audit | Logs/ZIP folder | Excel + PPT + CA commands | Audit configuration and profiles
2 Consistency Check | PRE and POST folders | 2 Excel + CC commands | Compare pre/post relations
3 Consistency Check (Bulk) | Multi-market root folder | Module 2 outputs per market | Run bulk comparison
4 Final Clean-Up | Final folder | Clean-up folder | Operational final clean-up